## Slide 1: Poke-Yoke for Safety Requirements

## Slide 2: PURPOSE
Kaizen events can be used as a workplace intervention to improve both productivity and safety
Often times when completing a 6S, the improvement team focuses on the reorganization to improve productivity and safety regulations can take a back seat
This PowerPoint is a quick refresher on common safety regulations and hazards to keep in mind when completing a Kaizen event

## Slide 3: FIRE EXTINGUISHERS
There is a 36” clearance around each fire extinguisher.

## Slide 4: WALKWAYS/EMERGENCY EXITS
Walkways and emergency exit(s) are accessible and workers know the appropriate route.

## Slide 5: EYEWASH STATIONS
There is a 36” clearance around each eyewash station.

## Slide 6: ELECTRICAL PANELS
The front of electrical panels has a minimum of three feet of clearance and a minimum width to be the width of the equipment or 2.5 feet, whichever is greater.

## Slide 7: AIR SHUT OFF VALVE
Air shut off point is within reasonable distance for employees: (tables should allow enough space if back to back and must not be too tall)

## Slide 8: PHONE/EMERGENCY LIST
There is a phone within reasonable distance from the workstation to be accessed for paging.
The emergency phone list is located near the phone.

## Slide 9: FORKLIFT TRAFFIC
Employees and/or equipment does not interfere with forklift traffic.
Blind corners are equipped with mirrors and/or warning signs.

## Slide 10: FIRE SPRINKLER/SPEAKERS
  All fire sprinkler heads have at least an 18” clearance below.
  Employees in the workstation are able to hear the speakers/horns (add or relocate speakers if necessary)

## Slide 11: FLOORING/TRIP HAZARDS
All floors are clean, dry, and slip resistant.
Air hose lines and electrical cords are not a trip hazard.

## Slide 12: STORAGE/LIGHTING
All storage racks are bolted down to ensure stability.
Site is properly lit